## Slide 1
Welcome to the NASA
Stennis Space Center
Construction Contractor Safety Orientation
Everyone is responsible for safety!

## Slide 2: Welcome
Welcome to John C. Stennis Space Center (SSC), America’s largest rocket propulsion test complex. As a member of the NASA family at SSC, you are joining a diverse group of individuals and a Center with a rich history.
Stennis is a unique “federal/commercial city,” with a combination of federal, state, and commercial organizations located throughout the Center. SSC was built in the 1960s to test the rockets that took Americans to the Moon. Today, we are the Nation’s premiere center for testing rocket engines.
Stennis Space Center is also dedicated to the OSHA VPP Star program. This commitment extends to all our contractors so that excellent safety and health performance is always our highest expectation.

## Slide 3: Welcome
We are excited to have you join the Stennis family, where the workforce is what makes the difference; and we are committed to the NASA values of safety, teamwork, integrity, and mission success.
In this safety orientation you will receive information that represents the rules, regulations, hazards and emergency information associated with our site.
Always remember that at our facility, safety is everyone’s responsibility!

## Slide 4: Welcome
There are knowledge checks throughout this presentation. There are 60 questions in total. Select the BEST answer. After each short question section, it’s followed by the correct answers.
Compare your answer to the correct one. Move through the entire presentation in the same manner.
Your supervisor will retain your signed sign-in sheet as proof of taking the SSC Construction Contractor Safety Orientation.

## Slide 5: Orientation Topics
Introduction
Arriving at the Center
Starting Work
Requirements and Regulations
Special Work
Emergencies
Danger and Hazard Warning Systems
Incident Reporting
General Rules and Responsibilities
Audits and Inspections

## Slide 6: Orientation Topics
Introduction
Arriving at the Center
Starting Work
Requirements and Regulations
Special Work
Emergencies
Danger and Hazard Warning Systems
Incident Reporting
General Rules and Responsibilities
Audits and Inspections

## Slide 7: Introduction
This presentation is designed to be used as a supplemental orientation to all established and existing safety plans and procedures for NASA, Stennis Space Center and Contractor/Subcontractor Safety Plans that are, “Submitted and Approved”
It is NOT intended to substitute the contractor's safety orientation, plan, or program and does not release the contractor or their employees from their legal obligation of conforming to federal, state and local safety and health standards to provide their employees with a safe and hazard free working environment

## Slide 8: Introduction
“Construction Site” – An area where construction activities are in progress including:
Contractor site managers/supervisors will ensure that all personnel working at SSC have completed this orientation training and OSHA 10 Hour Construction training prior to performing any work on site (management personnel must complete OSHA 30 hour construction training)
A copy of NASA Construction Safety and Health Program (SCWI-8715-0008) is available on the NASA Construction Safety website – regulatory references not included in this presentation can be found in this document
You and your employer are required to follow this SCWI and all applicable NASA work instructions
Failure to observe any of these rules or industry standards and regulations may result in immediate and permanent discharge from the job site
Key Regulations
and Requirements
29 CFR 1926
29 CFR 1910
SCWI
8715-0008
– | Construction | – | Renovation | – | Decorating
– | Excavation | – | Repair | – | Surveying
– | Alteration | – | Painting | – | Demolition

## Slide 9: Introduction
Stennis Space Center is a VPP Star Site?
  a. True b. False
All contractor personnel are required to completed this presentation?
  a. True b. False
Contractor personnel shall have an OSHA 10 or 30 hour course completion?
  a. True b. False
4. Failure to observe any safety rule or industry standard and regulation will result in immediate and permanent discharge from?
  a. The Military b. The Exchange c. The Office d. The Center

## Slide 10: Introduction
Stennis Space Center is a VPP Star Site?
  a. True b. False
All contractor personnel are required to completed this presentation?
  a. True b. False
Contractor personnel shall have an OSHA 10 or 30 hour course completion?
  a. True b. False
4. Failure to observe any safety rule or industry standard and regulation will result in immediate and permanent discharge from?
  a. The Military b. The Exchange c. The Office d. The Center

## Slide 11: Orientation Topics
Introduction
Arriving at the Center
Starting Work
Requirements and Regulations
Special Work
Emergencies
Danger and Hazard Warning Systems
Incident Reporting
General Rules and Responsibilities
Audits and Inspections

## Slide 12: Arriving at the Center
Stennis Space Center can be accessed from the South Gate using I-10 or the North Gate from I-59 using the MS Hwy 607 exit.
Upon arrival, all contractor employees are required to check in with our Security Services to receive their identification badge.
Once issued an access badge, you will be allowed to enter the facility during the prescribed period of time listed on the badge.
When driving on site, all traffic rules and
speed limits must be obeyed.
Failure to do so can result in traffic tickets and loss of driving privileges on-site.
North Gate
South Gate

## Slide 13: Arriving at the Center
Seatbelts will be worn at all times when in or operating any vehicle, heavy equipment or forklift
Use of a communication device (cell phone, radio, etc.) by the driver of any vehicle is prohibited, unless the vehicle is safely parked or the driver is using a hands-free device
Use of a communication device of any kind, whether hand-held or hands-free, by the driver of any vehicle entering or exiting through a security checkpoint is prohibited

## Slide 14: Arriving at the Center
Always be on the lookout for pedestrians, bicyclists and wildlife
The right of way belongs to all emergency vehicles when their lights are flashing and sirens are used
Park only in designated locations or approved areas
If you are unsure, ask your
supervisor
Be advised that government vehicle or assigned parking spaces are generally identified by a yellow parking barrier and yellow painted lines

## Slide 15: Arriving at the Center
5. Upon arrival you are required to check in with Security Services to receive a(n) ______?
    a. Car tag b. Registration c. ID badge d. Key to the Center
Failure to drive on site safely can result in traffic tickets and loss of driving privileges?
a. True b. False
7. Seat belts are required to be worn by all occupants when in a vehicle?
    a. True b. False
8. Use of a communication device of any kind is prohibited when entering and exiting a security check point?
    a. True b. False

## Slide 16: Arriving at the Center
5. Upon arrival you are required to check in with Security Services to receive a(n) ______?
    a. Car tag b. Registration c. ID badge d. Key to the Center
6. Failure to drive on site safely can result in traffic tickets and loss of driving privileges?
a. True b. False
7. Seat belts are required to be worn by all occupants when in a vehicle?
    a. True b. False
8. Use of a communication device of any kind is prohibited when entering and exiting a security check point?
    a. True b. False

## Slide 17: Orientation Topics
Introduction
Arriving at the Center
Starting Work
Requirements and Regulations
Special Work
Emergencies
Danger and Hazard Warning Systems
Incident Reporting
General Rules and Responsibilities
Audits and Inspections

## Slide 18: Starting Work
Meetings
Participation in daily and weekly safety meetings is a requirement of NASA
Always sign an attendance form when you attend any safety and health meetings to document your attendance
NASA and its On-site Prime Contractors will audit records periodically to ensure these meetings are held and that everyone on the job site has attended them

## Slide 19: Starting Work
Daily Safety Meeting
Will be held by the work activity/craft supervisor, foreman, or crew chief
Included topics:
  Communication from daily management meetings
  Basic job steps for the task/activity
  Potential hazards and corrective actions for each job step
  Activity Hazards Analysis reminders
  Multiple activities coordination
  Precautions, permits, PPE, barricades, energy isolation, etc.

## Slide 20: Starting Work
Activity Hazard Analysis
The AHA is specific to an activity and is called an Activity Hazard Analysis or Safe Plan of Action (SPA)
The AHA is a tool to review the activities being performed for the purpose of identifying all hazards of the activity and taking measures to protect employees and reduce risk
An AHA will be completed and discussed at the daily safety briefing prior to the commencement of daily work by the contractor initiating the activity
NASA will frequently check job sites to ensure an AHA has been completed for the work being performed

## Slide 21: Starting Work
Activity Hazard Analysis (AHA) Requirements
Specific safety and health measures necessary to mitigate hazards identified by the AHA will be documented on the AHA form
All workers will participate in developing and reviewing before signing the AHA
NASA will audit compliance to this requirement
The AHA MUST be updated as conditions or the job risks change from what was originally planned
An incomplete, inadequate or missing AHA can result in the job being stopped

## Slide 22: Starting Work
Activity Hazard Analysis Form
Hazard Identification and Corrective Actions
Reminders of NASA
Rules
Contractor Employee
Signatures

## Slide 23: Starting Work
Permits
Each AHA will identify necessary permits to perform the job safely
The following NASA permits are to be used when applicable:
  Confined Space Entry
  Hot Work
  Scaffold
  Digging
All permit areas must be completed
There should be no blank spaces and employees shall sign the permits when required, but only after they have been reviewed and approved

## Slide 24: Starting Work
Personal Protective Equipment (PPE)
The following is the minimum PPE required on every Construction site:
  Safety glasses with side shields
  Hard Hat
  Protective Toed Shoes
  High Visibility Safety Apparel
Additional protective equipment will be worn when applicable
The daily Activity Hazard Analysis process is to be used for determining additional PPE requirements

## Slide 25: Starting Work
Potential Hazards
All Construction employees need to be aware of the many types of hazards they may encounter at Stennis Space Center
These hazards include but are not limited to:
  Flammable materials such as Liquid Hydrogen and Isopropyl Alcohol
  Hazardous materials such as Liquid Oxygen, Hydrogen Peroxide, Asbestos, Lead Paint, and more
  Elevated work areas
  Traffic and roadways
  Electricity
  Underground piping and other hazards
  Waterways, ponds and canals
  Wildlife such as alligators, snakes, insects and other mammals

## Slide 26: Starting Work
We all have rules and procedures to follow which help keep us safe on the job!
Potential Hazards
Due to the various potential hazards at NASA , contractors are required to understand all applicable OSHA regulations related to their jobs and work areas
The same holds true for Contractor employees
Contractor employees are required to follow safe work practices established by their employer and as required by NASA
Failure to do so can result in removal from the site
Contractor employees and all levels of supervision are accountable to work safely at all times
When in doubt about safety or a safety requirement, ASK

## Slide 27: Starting Work
9. Participation in a weekly and daily safety meeting is a requirement of ______ ?
  a. The DOD b. NASA SSB c. NASA SSC
10. NASA and On-site Prime contractors will audit records to ensure meetings were held and full participation occurs?
  a. True b. False
11. An Activity Hazard Analysis (AHA) is specific to an activity and is sometimes called a Safe Plan of Action (SPA)? ?
  a. True b. False
12. An AHA is required to be completed and briefed prior to the start of any work
  a. True b. False

## Slide 28: Starting Work
9. Participation in a weekly and daily safety meeting is a requirement of ______ ?
  a. The DOD b. NASA SSB c. NASA SSC
10. NASA and On-site Prime contractors will audit records to ensure meetings were held and full participation occurs?
  a. True b. False
11. An Activity Hazard Analysis (AHA) is specific to an activity and is sometimes called a Safe Plan of Action (SPA)? ?
  a. True b. False
12. An AHA is required to be completed and briefed prior to the start of any work
  a. True b. False

## Slide 29: Starting Work
13. The following permits are to be used when applicable?
  a. Confined Space, Hot Work b. Scaffold c. Digging d. All Listed
14. The daily AHA is used to determine the PPE requirements on the job?
  a. True b. False
15. All construction personnel need to be aware of the many hazards they may encounter at Stennis Space Center?
  a. True b. False
16. Contractor personnel are required to follow safe work practices established by their employer and as required by NASA SSC?
  a. True b. False

## Slide 30: Starting Work
13. The following permits are to be used when applicable?
  a. Confined Space, Hot Work b. Scaffold c. Digging d. All Listed
14. The daily AHA is used to determine the PPE requirements on the job?
  a. True b. False
15. All construction personnel need to be aware of the many hazards they may encounter at Stennis Space Center?
  a. True b. False
16. Contractor personnel are required to follow safe work practices established by their employer and as required by NASA SSC?
  a. True b. False

## Slide 31: Orientation Topics
Introduction
Arriving at the Center
Starting Work
Requirements and Regulations
Special Work
Emergencies
Danger and Hazard Warning Systems
Incident Reporting
General Rules and Responsibilities
Audits and Inspections

## Slide 32: Requirements and Regulations
Hazard Communication - Safety Data Sheets
Contractors will provide all Safety Data Sheets (SDS) to NASA for approval prior to bringing any chemicals on site
  Contractors will maintain copies of SDS on site in a location which is accessible to all employees
A list of all contractor chemicals and matching SDS will be submitted to the NASA Industrial Hygiene (IH) Department
  Required within fourteen working days
If you have questions about the chemical you will be working with, check the SDS prior to starting the job

## Slide 33: Requirements and Regulations
Hazard Communication – Container Labeling
All containers, regardless of size and quantity, shall be labeled or tagged with the chemical name and hazard warning information, in accordance with 29 CFR 1910.1200
The National Fire Protection Association (NFPA) or the Hazardous Material Identification System (HMIS) labeling system is preferred on transfer containers
Any container equal to or greater than 55 gallons will use NFPA labeling

## Slide 34: Requirements and Regulations
Lead
All work involving lead-containing materials will be completed under a lead-compliance plan meeting the requirements of 29 CFR 1910.1025 & 29 CFR 1926.62
The contractor will submit documents showing that the employees performing work involving lead containing material are trained, have a current respirator fit test and hold a valid certificate
If an employee suspects that they have come into contact with lead, they will stop work and notify their supervisor

## Slide 35: Requirements and Regulations
Asbestos
Areas that have asbestos containing material such as fireproofing, piping insulation, floor tiles, ceilings, test stands, mechanical equipment rooms and other various locations have been identified
FIRE PROOFING
FLOOR TILES
PIPE INSULATION

## Slide 36: Requirements and Regulations
Asbestos
Work in areas that has the potential of disturbing asbestos containing material is regulated and will meet requirements of 29 CFR 1910.1001 and 29 CFR 1926.1101
The contractor will submit documents showing that the employees performing work involving asbestos are trained, have a current respirator fit test and hold a valid certificate
If an employee suspects that they have come into contact with asbestos, they will stop work and notify their supervisor

## Slide 37: Requirements and Regulations
Noise Hazards
Hazardous noise areas are posted in locations where the noise levels can be expected to be at or above 85 dBA
Hearing protection is mandatory in these areas
If you use any machinery or equipment that generates 85 dBA of noise or greater, you are required to wear proper hearing protection
For assistance with monitoring noise levels, you may contact a NASA Industrial Hygienist at 688-3173

## Slide 38: Requirements and Regulations
Respiratory Protection
The AHA will identify required PPE
An assessment of employee exposure is required to ensure respirators are properly selected and used
Submission of training, fit testing, and medical approval documentation is required for employees required to wear respiratory protection
Proper cleaning and storage of respiratory equipment is required by user
Respirators are to be used as a last resort
Engineering controls that eliminate or reduce the hazard to permissible levels must always come first

## Slide 39: Requirements and Regulations
Confined Spaces
Permit Required Confined Spaces are posted throughout the Center
Prior to entering a permit required confined space, a competent person will perform all necessary atmospheric tests using a properly calibrated instrument

## Slide 40: Requirements and Regulations
Confined Spaces
Contractors shall use only the NASA confined space permit or reclassification forms
If there are any questions about the confined space program at NASA , ask your supervisor to contact the Safety and Mission Assurance department designated for your project
For work in hazardous classification areas, special controls are necessary for portable electronics, tools/equipment, hot work, and other energized activities. Contractors shall follow procedures as directed in SCWI-8715-0012 Work in Hazardous Classifications

## Slide 41: Requirements and Regulations
Confined Spaces
Prior to work being performed in a hazardous or potentially hazardous atmosphere (i.e. confined space or process safety management covered system), a competent person shall perform all necessary tests using a properly calibrated instrument

## Slide 42: Requirements and Regulations
Hot Work
A hot work permit shall be requested from the Contractor Construction Manager or Fire Department (688-3639) for any activity where there is a source of ignition
Hot work permits (Form SSC-68) are required for:
Welding
Cutting
Grinding
Brazing
Any flame or sparking operation

## Slide 43: Requirements and Regulations
Hot Work
Atmospheric analysis is required for hot work that is within 50 feet from a propellant or fuel line
A competent person shall perform all necessary atmospheric tests using a properly calibrated instrument

## Slide 44: Requirements and Regulations
Powered Industrial Equipment
Pre-use inspections are required for all aerial lifts, fork lifts, and cranes
These inspections shall be documented and available for auditing purposes
No one shall operate powered industrial equipment unless they are trained in accordance with OSHA regulations and the training is current
Powered industrial equipment shall only be used for the purpose they have been designed for
All powered industrial equipment shall be in good repair and safe to use

## Slide 45: Requirements and Regulations
Fall Protection
Fall protection is required for all work performed on any unprotected platform at or above 6 feet in height
Fall protection is required on any ladder
higher than 20 feet
Fall protection is required when working on low-sloped roofs
A safety monitoring system is not an acceptable fall protection for small low sloped/flat roofs at SSC
A fall protection competent person is required for inspection of equipment and training
Fall arrest protection is required when operating an aerial lift

## Slide 46: Requirements and Regulations
Fall Protection
All employees who are exposed to fall hazards, utilize fall protection equipment and systems shall:
  Evaluate all work areas for fall hazards and ensure these hazards are properly controlled before work begins
  Follow NASA and OSHA requirements regarding the proper use, wear, inspection and maintenance of fall protection equipment
  Inspect before and after use of all fall arrest equipment for wear and possible damage and take out of service any suspect equipment
  Properly store and maintain fall protection equipment in a clean and dry condition
  Be properly trained in the recognition of fall hazards and use of fall protection equipment

## Slide 47: Requirements and Regulations
Electrical Safety
All Contractors shall follow the SCWI-8715-0006, SSC Electrical Safety Program requirements.
Energized work is not allowed at SSC, unless approved by Prime Contractor Safety, NASA Safety Support Contractor, NASA Operations and Maintenance Technical Authority, and SMA Electrical Subject Matter Expert.
No one will be allowed to work on or near live electrical equipment unless they are qualified to do so and have completed proper training and be Authorized to do the work.

## Slide 48: Requirements and Regulations
Electrical Safety
Personal Protective Equipment used to perform electrical work shall be in good working condition and shall meet current testing and inspection requirements per SCWI-8715-0006
GFCIs are required on all construction sites
Contractors shall follow the Assured Equipment Grounding Conductor Program per SCWI-8715-0006 requirements
All electrically driven equipment and power cords shall be in good condition and inspected prior to use
This inspection is to be documented on the AHA

## Slide 49: Requirements and Regulations
Scaffolding
100% fall protection is required in the assembly of scaffolding
All scaffolding must be erected under the supervision of a Competent Person
Scaffolding must be inspected and documented (tagging system) by a Competent Person before initial use, prior to every shift, and after all engine tests
Qualified scaffold erectors under the supervision of a competent person are the only personnel who can reconfigure or alter a scaffold

## Slide 50: Requirements and Regulations
Scaffolding
Employees will NOT use any scaffold that is not tagged or is tagged with a “Danger” tag
Scaffold Tags and descriptions:
  Green Tag – Scaffold is completed and safe for use
  Yellow Tag – Scaffold is incomplete, properly anchored fall protection may be required at all times
  Red Danger Tag – Scaffold is unsafe to use, in need of repair, incomplete, do not use

## Slide 51: Requirements and Regulations
Process Safety Management
The following areas contain highly hazardous materials which require application of the OSHA Process Safety Management Standard, 29 CFR 1910.119
  - All Test Stands (A1,A2,A3,B1,B2,E1,E2,E3, E4)
  - Cryogenic Facility
  - High Pressure Gas Facility
  - All Liquid Hydrogen Barges
No construction employee can enter or work in these areas without having received awareness training on the potential hazards associated with the PSM area and construction activities
Special work practices apply when working in these areas
51

## Slide 52: Requirements and Regulations
Fire Protection/Prevention
No smoking outside of designated smoking areas at the Center
Use only approved and properly labeled Safety cans for the storage and use of flammable materials
Contractors are to provide their own fire extinguishers for hot work activities
Facility fire extinguishers are not for
construction use
Fire extinguishers must be inspected daily and on a monthly basis

## Slide 53: Requirements and Regulations
Machine Guarding
Safeguards must meet these two basic minimum requirements:
  Prevent Contact: the safeguard must prevent hands, arms, fingers, or any body part from making contact with the point of operation hazard
  Secure: Workers should not be able to easily remove or tamper with a safeguard
Any machine or piece of equipment that is not adequately guarded shall be removed from service

## Slide 54: Requirements and Regulations
Excavation and Shoring
All trenching/excavation work deeper than 12 inches requires a NASA Dig Permit (Form SSC-618)
The dig permit will be reviewed and approved by Safety and Mission Assurance or designee, for all trenches/excavations
All trenches/excavations will be evaluated to determine if they meet the definition of a permit required confined space
No work is allowed to be performed in excavations or trenches until water is removed
All soil at is considered Type ”C” initially or until re-classified

## Slide 55: Requirements and Regulations
Signs and Barricades
Barricades, signs, and/or caution tape will be placed where necessary to warn and protect employees against hazardous conditions and activities such as overhead work, electrical work, and floor and wall openings and trenches
Appropriate warning signs and barricades will be posted to prevent unauthorized entry
Danger barricades or tape shall be physically labelled or identified by the contractor who installed it when working around multiple contractors

## Slide 56: Requirements and Regulations
Signs and Barricades
Barricade tape will be used only for the purpose for which it is designed
If, for example, danger do not enter tape is used, then no unauthorized person is allowed into the area unless they take the same precautions as those inside the barricaded area and they have permission to enter
Using the wrong type of signage and/or barricades is considered an unsafe practice and can lead to serious incidents on the job

## Slide 57: Requirements and Regulations
Lockout/Tagout
LO/TO will apply to authorized persons and affected personnel performing work at the site who install, repair, maintain, or inspect electrical, mechanical, hydraulic and/or pressure systems
Red locks are the only type of locks that are to be used for lockout at NASA
In addition to the red lock, contractors will affix a NASA approved lockout tag to the lock
These tags are available through the construction manager

## Slide 58: Requirements and Regulations
Lockout/Tagout
Contractors are subject to all the requirements of SCWI-8715-0013, Control of Hazardous Energy Lockout/Tagout and Non- Service/Maintenance Hazardous Energy Isolation
Every contractor employee relying on lockout for their protection will be represented by their own personal red lock and tag
Tags must be completed properly

## Slide 59: Requirements and Regulations
Lockout/Tagout
Each lock must be accompanied by Form –SSC 808 (DO NOT OPERATE TAG)
Tags that are used for LO/TO must be fully filled out and must be legible using a fine or extra fine permanent marker
Tagout Only
Tagout Only is using a tag as a device applied to an energy control point when a lock and tag is not feasible
It is used in conjunction with Lockout/Tagout procedures
Lockout/Tagout is the preferred method over Tagout Only
Standardized Lockout/Tagout Tag Form SSC 808

## Slide 60: Requirements and Regulations
17. Under the Global Harmonization System “Hazard Communication”, a _____ is required for chemicals brought on site?
  a. MDS b. SDM c. SDS d. MSDS
18. NASA requires all containers regardless of size to be properly labeled with the contents?
  a. True b. False
19. Any work involving Lead or Asbestos requires a Special Work Plan?
  a. True b. False
20. You are required to protect your hearing at any level is at or above __ dBA ?
  a. 75 b. 80 c. 85 d. 90

## Slide 61: Requirements and Regulations
17. Under the Global Harmonization System “Hazard Communication”, a _____ is required for chemicals brought on site?
  a. MDS b. SDM c. SDS d. MSDS
18. NASA requires all containers regardless of size to be properly labeled with the contents?
  a. True b. False
19. Any work involving Lead or Asbestos requires a Special Work Plan?
  a. True b. False
20. You are required to protect your hearing at any level is at or above __ dBA ?
  a. 75 b. 80 c. 85 d. 90

## Slide 62: Requirements and Regulations
21. Employees requiring respiratory protection must provide proof of training and ______?
  a. Fit testing and Medical b. Medical c. Mental d. All Listed
22. Permit Required Confined Space locations are posted throughout the Center?
  a. True b. False
23. All Confined Space entries require proper training?
  a. True b. False
24. All Hot Work requires a SSC Hot Work Permit?
  a. True b. False

## Slide 63: Requirements and Regulations
21. Employees requiring respiratory protection must provide proof of training and ______?
  a. Fit testing and Medical b. Medical c. Mental d. All Listed
22. Permit Required Confined Space locations are posted throughout the Center?
  a. True b. False
23. All Confined Space entries require proper training?
  a. True b. False
24. All Hot Work requires a SSC Hot Work Permit?
  a. True b. False

## Slide 64: Requirements and Regulations
25. Atmospheric analysis is required within _____ feet of a propellant line?
  a. 50 b. 75 c. 100 d. 150
26. All motorized equipment is inspected daily before use and documented?
  a. True b. False
27. Fall protection is required when working at heights of ____ feet or more?
  a. 3 b. 4 c. 5 d. 6
28. All electrical cords must have a Ground Fault Circuit Interrupter (GFCI) attached?
  a. True b. False

## Slide 65: Requirements and Regulations
25. Atmospheric analysis is required within _____ feet of a propellant line?
  a. 50 b. 75 c. 100 d. 150
26. All motorized equipment is inspected daily before use and documented?
  a. True b. False
27. Fall protection is required when working at heights of ____ feet or more?
  a. 3 b. 4 c. 5 d. 6
28. All electrical cords must have a Ground Fault Circuit Interrupter (GFCI) attached?
  a. True b. False

## Slide 66: Requirements and Regulations
29. Scaffold tag colors used at SSC are what colors?
  a. Green b. Yellow c. Red D. All Listed
30. All scaffolding will be inspected and the tag signed prior to use?
  a. True b. False
31. Fire extinguishers will be inspected daily and documented monthly?
  a. True b. False
32. Process Safety Management (PSM) areas requires special training?
  a. True b. False

## Slide 67: Requirements and Regulations
29. Scaffold tag colors used at SSC are what colors?
  a. Green b. Yellow c. Red D. All Listed
30. All scaffolding will be inspected and the tag signed prior to use?
  a. True b. False
31. Fire extinguishers will be inspected daily and documented monthly?
  a. True b. False
32. Process Safety Management (PSM) areas requires special training?
  a. True b. False

## Slide 68: Requirements and Regulations
33. Contractors are to provide their own fire extinguishers?
  a. True b. False
34. All digging 12 inches or more requires an SSC Dig Permit?
  a. True b. False
35. Danger barricades do not require contact information when installed around multiple contractors?
  a. True b. False
36. SSC Lock-Out and Tag-Out (LOTO) requires a SSC Tag and Red color lock?
  a. True b. False

## Slide 69: Requirements and Regulations
33. Contractors are to provide their own fire extinguishers?
  a. True b. False
34. All digging 12 inches or more requires an SSC Dig Permit?
  a. True b. False
35. Danger barricades do not require contact information when installed around multiple contractors?
  a. True b. False
36. SSC Lock-Out and Tag-Out (LOTO) requires a SSC Tag and Red color lock?
  a. True b. False

## Slide 70: Orientation Topics
Introduction
Arriving at the Center
Starting Work
Requirements and Regulations
Special Work
Emergencies
Danger and Hazard Warning Systems
Incident Reporting
General Rules and Responsibilities
Audits and Inspections

## Slide 71: Special Work
Personal Floatation Devices (PFD)
SSC has numerous canals and barges which pose potential fall exposures from unprotected edges into water
When working over water, on/around docks, bridges, etc. wearing a PFD is required
When selecting a PFD it must fit properly
Secure all straps, buckles and zippers
Check for tears, cuts, deterioration, leaks and damage
Inspect the PFD prior to and during each use

## Slide 72: Special Work
Pile Driving
Personnel Safety:
  Personnel shall not remain on top of piles during driving activities
  Hearing protection must be worn during pile-driving activities
Use of Prototype Equipment:
  Do not use prototypical pile-driving equipment at unless permission is obtained from the CO and NASA SMA
Moving Parts Guarding:
  Belts, gears, shafts, pulleys, sprockets, spindles, drums, fly wheels, chains, or other reciprocating, rotating, or moving parts or equipment will be guarded if such parts are exposed to contact by employees or may otherwise create a hazard

## Slide 73: Special Work
Pile Driving
Sheet Pile Activity: Must stop if winds exceed 20 mph
Heavy Clothing: In addition to head protection, eye protection, and foot protection, personnel engaged in stabbing piles will wear heavy shoes, heavy long-sleeved shirts, and heavy jeans or pants
Earth Drilling
All members of the drilling crews will be trained in:
  The operation, inspection, and maintenance of the equipment
  The safety features and procedures to be used during operation, inspection, and maintenance of the equipment
  Overhead electrical line and underground hazards
  Information contained in equipment manuals
  Activity Hazard Analysis specifics

## Slide 74: Special Work
Cranes
Prior to the use of any mobile crane brought to SSC, the Contractor will submit the following documentation to the Contracting Officer’s Representative (COR) for review:
  A copy of the crane’s annual inspection/certification
  Name and credential of the inspector(s)
  The crane operator’s current training certification
  Load tests

## Slide 75: Special Work
Cranes
Any crane requires a pre-use inspection
Advance notification is required and must be made to the COR at least 48 hours prior to such crane’s intended use so the inspection can be coordinated
This inspection must be completed by the COR or designee
In addition to the OSHA-required inspections of cranes, SSC requires a documented daily inspection of each crane prior to its use
These documents shall be maintained on the
construction site for audit purposes

## Slide 76: Special Work
Heavy Equipment
The contractor is responsible to ensure that all required inspections (daily or pre- use) of equipment are completed
Operators are to be certified to operate heavy equipment
Documentation of certification and training shall be available at the job site

## Slide 77: Special Work
37. When working over or near water you are required to have on a PFD?
  a. True b. False
38. The guarding of moving parts or machinery is not required?
  a. True b. False
39. All cranes require SSC permission. Submit the Crane Annual Inspection, Operators Medical Exam, Operators Training, and Load Tests ?
  a. True b. False
40. All rigging MUST be proof tested before it can be used at SSC ?
  a. True b. False

## Slide 78: Special Work
37. When working over or near water you are required to have on a PFD?
  a. True b. False
38. The guarding of moving parts or machinery is not required?
  a. True b. False
39. All cranes require SSC permission. Submit the Crane Annual Inspection, Operators Medical Exam, Operators Training, and Load Tests ?
  a. True b. False
40. All rigging MUST be proof tested before it can be used at SSC ?
  a. True b. False

## Slide 79: Orientation Topics
Introduction
Arriving at the Center
Starting Work
Requirements and Regulations
Special Work
Emergencies
Danger and Hazard Warning Systems
Incident Reporting
General Rules and Responsibilities
Audits and Inspections

## Slide 80: Emergencies
Important Phone Numbers
Fire, medical, or environmental emergencies, call:
  From a NASA Phone: 911
  From a Cell Phone: 228-688-3636
When reporting emergencies make sure all pertinent information is provided:
Location of emergency
Nature of emergency
Whether or not injuries are involved
Name of caller
Number calling from
Please stay on the line until all the information is provided

## Slide 81: Emergencies
On-Site Medical Care
The Clinic hours of operation are: 7:00 am to 3:30 pm, Monday – Friday
Injuries/illnesses experienced before or after clinic hours, or during holidays, will report to the Fire Department for initial evaluation and will be referred to off site treatment facilities as necessary
Off site medical treatment requires clearing through the SSC Clinic before returning to work

## Slide 82: Emergencies
41. Stennis Space Center Fire, Medical or Environmental emergency call 911 from a NASA SSC phone and 688-3636 from a cell phone?
  a. True b. False
42. SSC Clinic hours are 0700 am to 3:30 pm, Monday -Friday?
  a. True b. False
43. Off site medical treatment requires the employee to clear through the SSC Clinic before returning to the job site?
  a. True b. False
44. Who Reports any injury or incident to the Contracting Officer Representative (COR)?
  a. Supervisor b. Employee c. Friends d. Neighbors

## Slide 83: Emergencies
41. Stennis Space Center Fire, Medical or Environmental emergency call 911 from a NASA SSC phone and 688-3636 from a cell phone?
  a. True b. False
42. SSC Clinic hours are 0700 am to 3:30 pm, Monday -Friday?
  a. True b. False
43. Off site medical treatment requires the employee to clear through the SSC Clinic before returning to the job site?
  a. True b. False
44. Who Reports any injury or incident to the Contracting Officer Representative (COR)?
  a. Supervisor b. Employee c. Friends d. Neighbors

## Slide 84: Orientation Topics
Introduction
Arriving at the Center
Starting Work
Requirements and Regulations
Special Work
Emergencies
Danger and Hazard Warning Systems
Incident Reporting
General Rules and Responsibilities
Audits and Inspections

## Slide 85: Danger and Hazard Warning Systems
Expectations
Contractors shall be knowledgeable of the danger and hazard warning systems at SSC to include:
  - Engine Test Alarms
  - Lightning Alerts
  - Fire Alarms
  - Tornado Warnings

## Slide 86: Danger and Hazard Warning Systems
Engine Test Alarms
  Security controls access to these areas
    - Contractors are not allowed to enter test areas without undergoing special training such as process safety management overview and Test Stand Safety and Health
    - The use of access control badges and sign in is required for the test stands
  Personnel will not enter any area under an active warning, test or alarm without specific permission from test stand or Facility Manager
  Test alarms and warning systems will be covered in more detail during the area overview training required for the test stands

## Slide 87: Danger and Hazard Warning Systems
Lightning Alerts
Weather conditions will be monitored and operations shall cease during electrical storms or when lightning alerts are communicated
Here is a list of the types of alerts for lightning:
  For Lightning Advisory: “( Alert Tone) Attention all personnel. A Lightning Advisory has been issued for the Stennis Space Center. A Lightning Advisory means conditions exist that indicate lightning is possible for this location. Personnel should monitor conditions and be prepared to take protective measures if required.”
  Click the icons below to hear the alerts:

## Slide 88: Danger and Hazard Warning Systems
Lightning Alerts
  For Lightning Warning: “(Alert Tone) Attention all personnel. A Lightning Warning has been issued for the Stennis Space Center.“ A Lightning Warning means lightning, or the potential for lightning has been detected within 5 miles of the Stennis Space Center. All personnel shall immediately secure outside activities and take shelter in a secure location.
  Click the icons below to hear the alerts:

## Slide 89: Danger and Hazard Warning Systems
Lightning Alerts
  For All Clear: “( Alert Tone,) Attention all personnel. All Clear. All Lightning Advisories and Lightning Warnings have been cancelled for SSC.”
  Click the icons below to hear the alerts:

## Slide 90: Danger and Hazard Warning Systems
Fire Alarms
  Upon hearing a fire alarm within a building or structure, evacuate the building/structure using the prescribed evacuation route posted in the areas
  Proceed to the evacuation assembly/marshalling areas and remain there to
be accounted for
  Once located in the assembly area, it is your supervisor’s responsibility to account for you and report missing persons to the fire department
  You are to remain in the assembly area until an all clear is given

## Slide 91: Danger and Hazard Warning Systems
Tornado Warning
  “(Wail Alert Tone) Tornado warning. A tornado warning has been issued for this area”
  Personnel and contractors are to take cover in an interior hallway, closet or small room, away from windows
  If you are in a trailer, seek cover in the nearest NASA building
  If outdoors, the safest place to be is as low to the ground as possible, and away from objects that could become a hazard for you

## Slide 92: Danger and Hazard Warning Systems
45. Contractors are not required to be knowledgeable of warning systems at SSC?
  a. True b. False
46. NASA Lightning Warnings require all staff to stop outside activities and take shelter in a secure location?
  a. True b. False
47. When a fire alarm is activated, you are required to go to the _______?
  a. NEX b. Marshalling area c. Your vehicle d. Nearest office
48. Supervisors are required to account for all personnel in the marshalling area during a fire alarm?
  a. True b. False

## Slide 93: Danger and Hazard Warning Systems
45. Contractors are not required to be knowledgeable of warning systems at SSC?
  a. True b. False
46. NASA lightning warnings require all staff to stop outside activities and take shelter in a secure location?
  a. True b. False
47. When a fire alarm is activated, you are required to go to the _______?
  a. NEX b. Marshalling area c. Your vehicle d. Nearest office
48. Supervisors are required to account for all personnel in the marshalling area during a fire alarm?
  a. True b. False

## Slide 94: Orientation Topics
Introduction
Arriving at the Center
Starting Work
Requirements and Regulations
Special Work
Emergencies
Danger and Hazard Warning Systems
Incident Reporting
General Rules and Responsibilities
Audits and Inspections

## Slide 95: Incident Reporting
Mishap Reporting
All mishaps are immediately reported by telephone to the following (in order):
  Dispatch at 228-688-3636 (by cell phone) or 911 (by landline)
  CO or COR
  NASA Safety and Mission Assurance
A NASA Mishap Report (Form 1627) is completed for ALL incidents within the first 24 hours of any incident
All contractor employees are required to cooperate in the investigation process following an incident

## Slide 96: Incident Reporting
Close Call Reporting
The SSC Close Call Reporting System (CCRS) is used to report CCRS close calls
A CCRS close call is an hazard or condition that could result in an accident, injury, or illness
Reporting CCRS close calls is the best method to prevent accidents by correcting hazards before they result in injury, illness or damage
Posters and forms are in each building or call 228-688-2762
Incidents with no OSHA recordable injury/illness, no damage, or damage less than $20,000 is considered a NMIS close call and shall be reported on NASA Mishap Form 1627

## Slide 97: Incident Reporting
49. Incidents that do not result in an injury or property damage do not have to be reported.
  a. True b. False
50. Reporting Close Calls is the BEST method to prevent accidents by correcting hazards before they result in injury, illness or damage?
  True b. False
51. A Form 1627 is required to be submitted _______ after the incident. ?
  a. 24 Hours B. 48 Hours C. One Week D. One Month
52. Once a mishap occurs, who should be contacted by the Contractor first?
  a. CO/COR b. NASA SMA c. Dispatch d. Subcontractor

## Slide 98: Incident Reporting
49. Incidents that do not result in an injury or property damage do not have to be reported.
  a. True b. False
50. Reporting Close Calls is the BEST method to prevent mishaps by correcting hazards before they result in injury, illness or damage?
  a. True b. False
51. A Form 1627 is required to be submitted _______ after the incident. ?
  a. 24 Hours B. 48 Hours C. One Week D. One Month
52. Once a mishap occurs, who should be contacted by the Contractor first?
  a. CO/COR b. NASA SMA c. Dispatch d. Subcontractor

## Slide 99: Orientation Topics
Introduction
Arriving at the Center
Starting Work
Requirements and Regulations
Special Work
Emergencies
Danger and Hazard Warning Systems
Incident Reporting
General Rules and Responsibilities
Audits and Inspections

## Slide 100: General Rules and Responsibilities
General Rules
Smoking is only allowed in designated areas only
The use of alcohol or unauthorized drugs or substances is prohibited
All caution, warning and danger signs, sirens, bells and other safety warnings
must be adhered to
Makeshift climbing devices in place of approved ladders, stands, or lifts are prohibited
All air or electrically driven tools will be completely
stopped and deactivated when unattended
Jewelry should not be worn around moving machinery, electrical systems, climbing, handling heavy objects or operating heavy machinery
Repeated safety infractions will not be tolerated

## Slide 101: General Rules and Responsibilities
Eyewash Stations/Safety Showers
The Contractor will ensure that eyewash stations and safety showers are available when contractor employees must work with hazardous materials that are harmful to the eyes and/or body
If indoors, always check with the building Facility Manager before testing any safety shower and eye wash station
You must test the eyewash station/safety shower prior
to beginning your work assignment
Know the location of eyewash stations and safety showers in your work area
If you come in contact with a chemical, flush your eyes or shower for a minimum of 15 minutes and remove all contaminated clothing

## Slide 102: General Rules and Responsibilities
Temperature Stress
Exposure to hot and cold and heat stress is addressed in the AHA
While working in cold weather:
  Dress in layers – remember to always wear your high visibility safety vest on the outside of all clothing
  Limit exposed skin
When working in hot weather:
  Stay hydrated
  Take frequent breaks in the shade
  Follow requirements of SCWI-8715-0014 – SSC Heat Stress Program

## Slide 103: General Rules and Responsibilities
Fire Extinguisher Use
Any contractor employee who is required to use a fire extinguisher to perform hot work duties or in the event of an emergency, shall be trained on their use
For most hand held extinguishers you have less than one minute of operation
Make sure help is on the way by calling 911 before using any fire extinguisher
Select the correct extinguisher for the class of fire
Notify your supervisor so the extinguisher can be replaced or recharged if it has been used or is found to be defective
Contractors shall not use NASA fire extinguishers for hot work activities
Contractors will provide their own fire extinguishers for hot work

## Slide 104: General Rules and Responsibilities
Welding Safety
Obtain Hot Work Permit (Form SSC-68) for each job
Inspect all equipment before use – do not use damaged or defective equipment
Remove or cover all combustibles within 35 feet of welding activities
Secure compressed gas cylinders for transportation with caps on (except when on the weld truck)
Store oxygen and acetylene bottles 20 feet apart or separated by a non-combustible barrier at least 5 feet high and having a fire-resistance rating of at least one-half hour
Use proper welding PPE
A fire watch is required to remain 30 minutes after welding activities

## Slide 105: General Rules and Responsibilities
Safe Atmospheric Verifications
All atmospheric monitors MUST be approved prior to initial use
Prior to work being performed in a hazardous or potentially hazardous atmosphere (i.e. confined space or process safety management covered system), a competent person will perform all necessary tests using a properly calibrated instrument
Atmosphere is hazardous when it’s:
  Oxygen deficient <19.5% oxygen
  Oxygen enriched >23.5% oxygen
  Flammable/Explosive – Lower Explosive Limit above 10%
  Toxic – above Permissible Exposure Limit or Immediately Dangerous to Life and Health

## Slide 106: General Rules and Responsibilities
Severe Weather Plan
In the event of a severe storm warning, the contractor will:
  Secure outside equipment and materials
  Place materials subject to damage in protected locations
  Check surrounding areas including roof, scaffolds and elevated work structures for loose material, equipment, debris and other objects that could be a high wind hazard
  Ensure that temporary erosion controls
are in place
High winds greater than 20 mph – no scaffold or elevated work is allowed in high wind conditions

## Slide 107: General Rules and Responsibilities
Portable Ladders
Use only industrial type rated ladders with all attached legible stickers
Inspect the ladder before each use
Only one person should be on a ladder at a
Time
Maintain 3 points of contact at all times
Secure extension ladders and extend 3 feet above upper landing
Use ladders with non-conductive railings near energized circuits
Do not carry tools or equipment in hand when
ascending or descending a ladder

## Slide 108: General Rules and Responsibilities
Ground Fault Circuit Interrupter (GFCI)
GFCI or an Assured Equipment Grounding Program will be used on all construction sites at
A GFCI will be used with all extension cords
Only industrial rated extension cords will be used 10,12,14 AWG
All cords shall be inspected prior to use and be free of defects
Electrical tape repairs are not authorized
Portable/hand held power tools shall have a grounding prong or be labeled as double insulated

## Slide 109: General Rules and Responsibilities
Radiation/Lasers
NEVER go over, under or through radiation barricades
OBEY all Radiation signs
The use of lasers as tools on construction sites require the contractor to have established written procedures for:
  Restriction of laser use to “qualified” persons
  Minimizing direct eye potential (verifying beam path prior to firing, consideration of beam termination, not positioning at eye level, prohibiting intentional direct viewing)
  Prohibited times of use (dusk or night)

## Slide 110: General Rules and Responsibilities
Traffic Control Plan
A traffic control plan will be submitted to COR or designee for review and approval when working on or within 15 feet of a traveled roadway
Temporary traffic control methods will be used as described in the Department of Transportation Manual on Uniform Traffic Control Devices
This activity can only be conducted with written approvals

## Slide 111: General Rules and Responsibilities
Personal Clothing
Pants will be full length in construction areas and industrial shops (no cut-offs, shorts etc.)
Shirts will be, at a minimum, comparable to a “T” shirt with sleeves (no tank tops, net shirts, cut off shirts, sleeveless shirts, etc.)
Shirts will be tucked into slacks when working around rotating/moving equipment

## Slide 112: General Rules and Responsibilities
Housekeeping
Inspect your work area before the job is started and ensure that the area is clean and safe
All debris will be kept cleared from work areas, passageways and stairs
Do not block/lock exit doors
At the end of the workday, take the time to inspect your area and pickup, cleanup, and store any material or tools you used on the site

## Slide 113: General Rules and Responsibilities
Bloodborne Pathogens
Bloodborne pathogens are organisms that can cause diseases
Bloodborne pathogens can be carried in blood or many bodily fluids
Do not clean up spilled bodily fluids unless you are trained and authorized to do so and call for assistance when needed

## Slide 114: General Rules and Responsibilities
Buddy System
“Buddies” are expected to monitor and stay close in the event of an emergency, monitor safety behavior, and follow safety procedures
Contract workers will utilize the “Buddy System” when duties require an employee to work in remote, isolated, or otherwise non-observable locations
At a minimum, two (2) qualified persons are required for work over 600V and work on energized electrical systems
Supervisors will ensure such employees are readily observable or accounted for by other means (i.e., periodic radio/telephone “check in”)

## Slide 115: General Rules and Responsibilities
Motor Vehicle & Equipment Operation
Vehicle operators will be properly licensed and trained
Seatbelts will be worn at all times
A daily inspection of Heavy Equipment vehicles will be conducted and documented to assure safe operating condition
All vehicles/equipment will be turned off when unattended
Report vehicle accidents immediately
Use spotter or perform a safety check before backing up vehicle

## Slide 116: General Rules and Responsibilities
Motor Vehicle & Equipment Operation
Slow moving vehicle signs will be mounted on vehicles designed to be driven at speeds less than 25 mph
Parking of non-emergency equipment in emergency areas is prohibited
Parking is prohibited within 15 feet of a fire hydrant, fire department connection,
fire lane or any fire suppression system
Use of a communication device (cell phone, radio, etc.) by the driver of any vehicle is prohibited, unless the vehicle is safely parked or the driver is using a hands-free device
Use of a communication device of any kind, whether hand-held or hands-free, by the driver of any vehicle entering or exiting through a security checkpoint, is prohibited

## Slide 117: General Rules and Responsibilities
Outdoor Hazards
Always take proper precautions when working in outdoor areas and note that the following can be present on site:
  Stinging/biting insects: wasps, bees, hornets, ticks and mosquitoes
  Spiders, snakes, alligators, wild boar, and deer
  Poisonous plants
Do not feed the wildlife

## Slide 118: General Rules and Responsibilities
Imminent Danger Situations
All employees and sub contractors have the authority and responsibility to “Stop Work” that is judged to be immediately dangerous to life and health (IDLH), could cause major damage to system/facilities, or endanger the ability of to accomplish its mission
Any individual who stops an unsafe operation where imminent danger is involved, will immediately notify the manager and safety manager of that organization

## Slide 119: General Rules and Responsibilities
53. Each contractor shall be knowledgeable of their Sever Weather Plans ?
  a. True b. False
54. All portable ladders are required to be inspected prior to use?
  a. True b. False
55. Traffic control plans are required to be submitted if working within ______ of a traveled roadway?
  a. 10 feet b. 15 feet c. 300 feet d. One mile
56. Shorts and tennis shoes are allowed at construction sites when work is not being performed?
  a. True b. False

## Slide 120: General Rules and Responsibilities
53. Each contractor shall be knowledgeable of their Sever Weather Plans ?
  a. True b. False
54. All portable ladders are required to be inspected prior to use?
  a. True b. False
55. Traffic control plans are required to be submitted if working within ______ of a traveled roadway?
  a. 10 feet b. 15 feet c. 300 feet d. One mile
56. Shorts and tennis shoes are allowed at construction sites when work is not being performed?
  a. True b. False

## Slide 121: General Rules and Responsibilities
57. The buddy System is required if an employee is working in a remote, isolated or non-observable location?
  a. Sometimes b. Never c. Always
58. Fire extinguishers can be blocked as long as everyone knows where they are?
  a. True b. False
59. Never block an Exit ?
  a. True b. False
60. Snakes, bees, spiders, and gators may be present at SSC and pose a hazard to employees?
  a. True b. False

## Slide 122: General Rules and Responsibilities
57. The buddy System is required if an employee is working in a remote, isolated or non-observable location?
  a. Sometimes b. Never c. Always
58. Fire extinguishers can be blocked as long as everyone knows where they are?
  a. True b. False
59. Never block an Exit ?
  a. True b. False
60. Snakes, bees, spiders, and gators may be present at SSC and pose a hazard to employees?
  a. True b. False

## Slide 123: Orientation Topics
Introduction
Arriving at the Center
Starting Work
Requirements and Regulations
Special Work
Emergencies
Danger and Hazard Warning Systems
Incident Reporting Systems
General Rules and Responsibilities
Audits and Inspections

## Slide 124: Audits and Inspections
Audits
NASA and their On-Site Prime Contractor Safety and Mission Assurance Offices will perform random and frequent audits of contractor job sites
Findings of jobsite audits can delay projects, stop work, and/or result in removal from site
Each and every contractor employee shares in the accountability process for safety and health on the job site
Inspections
Daily informal inspections will be performed prior to beginning any definable feature of work
Contractors will formally inspect the job site at least weekly for hazards and failures in safety, health, and environmental requirements
Contractors are responsible to ensure that all required inspections (daily or pre-use) of equipment are completed
– These include but are not limited to lift trucks, cranes, scaffolds, aerial lifts, PPE, earth-drilling equipment, and fire extinguishers

## Slide 125: Closing Statements
Thank you for your cooperation…
Remember to always follow all safety and health procedures and rules
Be sure to review and sign the AHAs
Reference SCWI-8715-0008 and 29 CFR 1926 for construction safety requirements
If you have any questions, start with your supervisor and safety and health
representative first
Finally, work safely at all times, remember to report close calls and mishaps immediately, and know that you have to stop work during any unsafe operation